Title: Electronic thermal conductance in graphene via electrical noise

Abstract

Intro

Chapter: Johnson noise thermometry
outline the basic idea and strict requirements of measuring temperature in 2D systems. Need something non-invasive, layer distinguishing, and electron/phonon distinguishing. Radiation thermometry meets all these requirements. Johnson noise is analogous to this

Section: thermal noise in resistors
history of Johnson-Nyquist noise. Derive voltage fluctuations historically: first thermodynamically, then fluctuation dissipation, then microscopically. Gaussian distributed.

Section: noise in resistor networks “The Johnson noise temperature”
copy from geometric factor: What happens when we have many resistors with different R and T. When adding two Gaussians together you add the means and the variances. Therefore, if two resistors are in series, their noise fluctuations combines by add their voltage squared fluctuations. Similarly in two resistors in parallel you will add their current squared fluctuations. Introduce the concept of a Johnson noise temperature.

Subsection: resistors in series
copy from geometric factor. But include the formula for power.

Subsection: resistors in parallel
copy from geometric factor. But include the formula for power.

Subsection: arbitrary resistor networks
motivate the power dissipation formula for arbitrary networks.

Section: Johnson noise in RF circuits
derive power formulation of Johnson noise with a gamma term. argument why gamma must always be symmetric in 2 port device (transmission line in and out both terminated by R and T). Argument why noise power must be the same for any 2 devices with same 2 port R. Talk about impedance matching (not necessarily specifics but in concept). high frequency limits of Johnson noise. Prober’s low temperature paper. Show high level schematic (APL fig 1a)

Section: uncertainty in noise measurements.
Even noise has noise. There are 2 main areas of uncertainty in a noise measurements: The first comes from the fact that noise is stochastic and deals with how well you know the variance of a Gaussian after measuring some amount of time. If the measurements you take are discrete and uncorrelated then we get the usual 1/sqrt(n) but what to do if we are measuring a continuous signal. Problem stems back to (year) (cite bell labs paper) and n is given by the time bandwidth product.
The second source of uncertainty comes from external noise sources such as amplifiers and boils down to the question of the noise you measure, what amount comes from the sample. This can be seen as a constant offset to the sample temperature Tn. Show plot of noise vs T with offset. When we extrapolate the sample temperature to zero we find an offset due to other noise sources. This external noise modifies the uncertainty equation to (noise formula). Show plots of 2 signals with different bandwidths. Show fixed bandwidth over time.

Section: impedance matching
impedance matching mesoscopic devices has a unique set of challenges: 2-terminal resistance can vary significantly with gate and field, matching circuit must be constant down to cryogenic temperatures, insensitive to strong fields.

Subsection: LC tank circuits
theory of LC tank matching. Show equations for Z(f). plot real an imaginary impedance verse frequency with crossing at 50+0i. Show equations finding L and C given f0 and R. Show S11 for fixed R sweeping C. Show fixed LC sweeping R.
To make components temperature and field insensitive must use non ferrite. Give component names and numbers. Show a plot of temperature stability

Subsection: multi-stage matching
If resistance will vary by multiple orders of magnitude (e.g. magneto resistance) multi-stage matching networks can be used. Multi-stage LC networks allow you to cover a wider area of the resistance-frequency space by giving you multiple solutions of Z=50. Cell phones use many stages to capture the full range of the human voice (need source). If the resistance of the device is fixed we can use multi-stage matching to increase the bandwidth over which we are matched. Show real and imaginary components for single vs double stage matching (subtract off 50 to show how these are zeros). In this plot there are 2 solutions to Z = 50. In the R-f plane this looks like (show color plot of solution)
However, if instead we want to match to larger range of resistances, we can move one of these zeros to a higher resistance. This increases the dynamic range of the matching circuit at the expense of bandwidth.

Section: effective noise temperature
The effective noise temperature is the sum of all (unwanted) noise in your system in units of the sample noise temperature. Your signal to noise ratio is given by T/Tn. Tn is a function of gamma integrated over all frequencies. Show formula for. In practice the frequencies integrated over are determined by filters.

Section: Calibration
Since the gain and noise temperature of the circuit are a function of many complicated factors (stray, loss, gain profiles, noise profiles) it is necessary to calibrate. Furthermore its strongly dependent on the device resistance and therefore must be calibrated for every device/measurement circuit. Goal is to focus here on general calibration not graphene specifics,calibration of graphene will get its own chapter.

Section: Cross-correlated noise thermometry
One challenge in noise measurements is identifying the noise you wish to measure from the unwanted background noise. In the right circumstances, cross-correlation can used to average out unwanted noise leaving behind.
The idea is to send the noise from the device into 2 independent channels and if the noise on each channel is uncorrelated then you win. Describe the idea in the perfect world. Show schematic (APL fig 1b). using this you can remove the offset from the amplifiers (APL fig 2). However, this does not reduce the precision of the measurement. The integration time needed to attain a given uncertainty is not reduced (APL fig 3)

Subsection: multi-terminal cross-correlation
If cross correlation is used on multiple terminals the overlapping noise can be found similar to the Johnson noise temperature.
Chapter: Electronic cooling pathways in graphene
If we heat the electronic system, how is that heat conducted to the bath.

Section: Wiedemann-Franz
basic mechanism. Electron carry heat away through conduction. Each particle carries a fixed charge and fixed heat capacity. Include equation. Discuss assumptions. Show plot of experimental agreement.

Subsection: Linearization

Subsection: “Hot electron shot noise”

Section: Electron-Phonon coupling
general form including delta and Sigma_elph.

Subsection: Linearization

Subsection: Bloch-Gruneisen temperature

Subsection: Acoustic phonon

Subsection: Intrinsic optical phonons

Subsection: Remote optical phonons
include some table keeping track of the power laws

Section: Photon cooling
This is Johnson noise and its what you measure

Section: Heat transfer equations
total heat transfer for the entire system Q=…
formulate kappa equations for general steady state heating profile

Chapter: Thermal conductance via electrical noise
from eq above we see we need apply some sort of known heating profile and then measuring the resulting temperature rise. Define thermal conductance as Q/T_JN

Section: rectangular device
start by just walking through joule heating a rectangular device where the JN temp is the mean temp.

Subsection: Electronic conduction only
in the absence of phonons the problem can be solved analytically. Derive temperature profile. Show temperature profile. The mean temperature is the JN temperature. The thermal conductance has the usual geometric factors but with an extra factor of 12. If the WF law is formulated as the 2-terminal resistance it gives you the thermal conductance but for this 12. This 12 is related to how electric R is being measured by applying a voltage difference between the terminals while the thermal conductance is via this parabolic profile.

Subsection: Phonon cooling
If phonons dominate the profile is flat and we cannot effectively measure kappa. However in this limit we can measure the Sigma_elph and delta.

Section: Wedge: Johnson noise temperature vs mean temperatures
unlike the simple rectangle where the Johnson noise temperature was simply the mean temperature, for more complicated geometries we have to compute what effective temperature we will measure in a noise experiment given the temperature profile. The wedge can be solved analytically. If we use the definition G_{th} above we see again that in the limit of no phonons, the thermal conductance relates to kappa the same way as electrical conductance relates to sigma but with an extra factor of 12.
In the phonon limit however, the temperature is no longer flat as the current density is no longer uniform

Section: Arbitrary shapes: the geometric factor $\alpha$
For arbitrary shapes where analytic solutions do not exist we can turn to finite element simulations. We find this factor of 12 to be a universal property of 2-terminal devices, independent of geometry.

Section: circuitry

Chapter: Hydrodynamic theory of transport
explain the problem of transport. Build up historically. Drude. Fermi liquid. Interaction become dominate.

Section: Hydrodynamic framework
inspiration from Subir’s old papers and andy’s papers

Section: Experimental evidence
GaAs. Other 2 papers.

Chapter: RF cryostats and circuitry

Section: Janis

Section: Oxford

Section: Leiden

Section: JNT circuits

Chapter: Calibration of graphene devices

Chapter: Thermal conduction in high density graphene
all the data on Aria

Section: Device characteristics

Section: circuitry

Section: Low temperature Wiedemann-franz

Section: High temperature electron-phonon

Chapter: The Dirac fluid
charge neutral strongly interacting fluid of relativistic particles

Chapter: Magneto-thermal transport

Chapter: Future goals ????

Conclusions

Appendix:

A: Total noise vs gamma (effective noise model)
In the effective noise model we care about whether the backwards noise from the amplifier is greater or lesser than the sample temperature. Show as T is raised the dependence on gamma inverts.

B: components lists