Abstract

Intro

Chapter: Johnson noise thermometry
outline the basic idea and strict requirements of measuring temperature in 2D systems. Need something non-invasive, layer distinguishing, and electron/phonon distinguishing. Radiation thermometry meets all these requirements. Johnson noise is analogous to this

Section: thermal noise in resistors
history of Johnson-Nyquist noise. Derive voltage fluctuations historically: first thermodynamically, then fluctuation dissipation, then microscopically. Gaussian distributed.

Section: noise in resistor networks
copy from geometric factor: What happens when we have many resistors with different R and T. When adding two Gaussians together you add the means and the variances. Therefore, if two resistors are in series, their noise fluctuations combines by add their voltage squared fluctuations. Similarly in two resistors in parallel you will add their current squared fluctuations. Introduce the concept of a Johnson noise temperature.

Subsection: resistors in series
copy from geometric factor. But include the formula for power.

Subsection: resistors in parallel
copy from geometric factor. But include the formula for power.

Subsection: arbitrary resistor networks
motivate the power dissipation formula for arbitrary networks.

Section: Johnson noise in RF circuits
derive power formulation of Johnson noise with a gamma term. argument why gamma must always be symmetric in 2 port device (transmission line in and out both terminated by R and T). Argument why noise power must be the same for any 2 devices with same 2 port R. Talk about impedance matching (not necessarily specifics but in concept). high frequency limits of Johnson noise. Prober’s low temperature paper.

Section: uncertainty in noise measurements.
Even noise has noise. There are 2 main areas of uncertainty in a noise measurements: The first comes from the fact that noise is stochastic and deals with how well you know the variance of a Gaussian after measuring some amount of time. If the measurements you take are discrete and uncorrelated then we get the usual 1/sqrt(n) but what to do if we are measuring a continuous signal. Problem stems back to (year) (cite bell labs paper) and n is given by the time bandwidth product.
The second source of uncertainty comes from external noise sources such as amplifiers and boils down to the question of the noise you measure, what amount comes from the sample. This can be seen as a constant offset to the sample temperature Tn. Show plot of noise vs T with offset. When we extrapolate the sample temperature to zero we find an offset due to other noise sources. This external noise modifies the uncertainty equation to (noise formula). Show plots of 2 signals with different bandwidths. Show fixed bandwidth over time.

Section: impedance matching
impedance matching mesoscopic devices has a unique set of challenges: 2-terminal resistance can vary significantly with gate and field, matching circuit must be constant down to cryogenic temperatures, insensitive to strong fields.

Subsection: LC tank circuits
theory of LC tank matching. Show equations for Z(f). plot real an imaginary impedance verse frequency with crossing at 50+0i. Show equations finding L and C given f0 and R. Show S11 for fixed R sweeping C. Show fixed LC sweeping R.
To make components temperature and field insensitive must use non ferrite. Give component names and numbers. Show a plot of temperature stability

Subsection: Multi-stage matching
If resistance will vary by multiple orders of magnitude (e.g. magneto resistance) multi-stage matching networks can be used. Multi-stage LC networks allow you to cover a wider area of the resistance-frequency space by giving you multiple solutions of Z=50. Cell phones use many stages to capture the full range of the human voice (need source). If the resistance of the device is fixed we can use multi-stage matching to increase the bandwidth over which we are matched. Show real and imaginary components for single vs double stage matching (subtract off 50 to show how these are zeros). In this plot there are 2 solutions to Z = 50. In the R-f plane this looks like (show color plot of solution)
However, if instead we want to match to larger range of resistances, we can move one of these zeros to a higher resistance. This increases the dynamic range of the matching circuit at the expense of bandwidth.

Section: effective noise model
Section: effective noise temperature
The effective noise temperature is the sum of all (unwanted) noise in your system in units of the sample noise temperature. Your signal to noise ratio is given by T/Tn
includes gamma and is integrated over all frequencies. Show formula for
In practice the frequencies integrated over are determined by filters.

Section: Calibration

Chapter: Thermal conductance

Chapter: Electronic cooling in graphene

Chapter: Experimental apparatus

Section: Janis

Section: Oxford

Section: Leiden

Chapter: Dirac Fluid

Chapter: Magneto-thermal transport

Conclusions

Appendix:

A: Geometric factor

B: Total noise vs gamma
In the effective noise model we care about whether the backwards noise from the amplifier is greater or lesser than the sample temperature. Show as T is raised the dependence on gamma inverts.